## Slide 1
CLUSTER ANALYSIS
STORM microscopy and cluster analysis for PcG studies
Laura Martin, Álvaro Castells-García, Maria Pia Cosma, and Maria Victoria Neguembor
Visual instructions by Laura Martin, February 2022 1st 2022

## Slide 2
CLUSTER ANALYSIS
Cluster Analysis is used to identify regions of high density of signals in super resolution images taken with STORM
In STORM, molecules of interest are labelled with fluorophores and imaged.
The light signal of the fluorophores is registered as a list of “localizations”
Localizations are the coordinates x,y (and z if performed in 3D) of the light signal in the field imaged.
Localizations info is stored in .bin files.
We give these .bin files to the CLUSTER_ANALYSIS_Main.m matlab code (formed by several functions).
The code will finally identify bigger and smaller high density regions, called Islands and Clusters, respectively.

## Slide 3
CLUSTER ANALYSIS
Original script from Carlo Manzo
Modified in the years by J Otterstorm, J Borbely, A Castells, & L Martin
20 functions

## Slide 4
CLUSTER ANALYSIS
>CLUSTER_ANALYSIS_main
>defineClustersStruct
    >FindClusterStruct
>FindClusters
>saveClusterMetricData
    >extractClusterStats
        >DistanceDualColor
Hierarchical code organization of main functions
Set analysis parameters
Identifies Islands and clusters
Calculates clusters’ features:
n° localizations
Areas
NND (of In-Island only)
Calculates the global NND
between ALL clusters
Saves output files
(.xyn, .mat, .bin, .dcc, .fig, .png)
For detailed organization see ___Informtion about CLUSTER_code.docx

## Slide 5
CLUSTER ANALYSIS
Cluster Analysis requires the input of several parameters that can affect deeply the process of Islands and Clusters identification

## Slide 6
CLUSTER ANALYSIS
Values depending on Microscope/Camera settings
CRUCIAL FOR CLUSTER ANALYSIS
Optionals
Computational settings
Options for 3D images
Extra optional plots

## Slide 7
CLUSTER ANALYSIS
HOW DOES THE CODE WORK?

## Slide 8
CLUSTER ANALYSIS
1
pixel
160nm
First of all we have to define the size and resolution of our .bin file of localizations
In general, it is 256x256 px, 1px=160nmx160nm
.bin file of localizations

## Slide 9
CLUSTER ANALYSIS
10 nm
Before starting the cluster analysis, we enlarge the image of a zoom factor= original/analysis px_size
In this example, the zoom is 16X.
The pixel are now smaller,
measuring only 10nm x 10nm.

## Slide 10
CLUSTER ANALYSIS
2
1
2
1
3
4
2
1
2
2
1
2
4
1
2
1
32
1
1
1
1
4
We now create a density map based on local density of localizations.
To do this, we have to define the extent of the region considered as “local”.
In this example, we define it as the area of 5px x 5px surrounding each pixel. In this area, we count the number of localizations, we sum them, and we assign the number to the central pixel.
We repeat the procedure for each pixel.
We will have a matrix of size 4096 x 4096
[256 px x16 zoom factor = 4096 x 4096 pixels (each of 10nm)]
The values of the matrix are the sum of localizations around each pixel.

## Slide 11
CLUSTER ANALYSIS
2
1
2
1
3
4
2
1
2
2
1
2
4
1
2
1
32
1
1
1
1
4
We will have regions of HIGH density and regions of LOW density

## Slide 12
CLUSTER ANALYSIS
2
1
2
1
3
4
2
1
2
2
1
2
4
1
2
1
32
1
1
1
1
4
ISLAND
Empty
region
After summing localizations, we have to discriminate between high and low density. For this, we set a threshold.
If the value of a pixel is now below that threshold (i.e. <5), that pixel is discarded from the cluster analysis

## Slide 13
CLUSTER ANALYSIS
10 nm
The localizations inside the pixels discarded (low density), are discarded forever.
After the threshold, a binary mask is created.
Pixels becomes 0 and 1.
-0 pixel are discarded.
-1 pixels (=mask)are kept and analysed.
The filtered localizations, belonging to pixels kept, will be analysed to identify:
ISLANDs
CLUSTERs

## Slide 14
CLUSTER ANALYSIS
10 nm
ISLANDs
Are regions of the cell
with high density of localizations.
CLUSTERs
Are small regions with HIGH local density of localizations inside an ISLAND

## Slide 15
CLUSTER ANALYSIS
ISLANDs are defined first.
Inside ISLANDs we look for CLUSTERs
Super-resolution image
reconstruction
Cluster identification
ISLANDs
SINGLE
Cluster
CLUSTER
InIsland
Inside ISLANDs we have n CLUSTERs.
They are called CLUSTERs InISLAND
Inside ISLANDs we only have 1 cluster, thus this island is not called ‘island’ anymore, but becomes a
SINGLE CLUSTER
(=ISLAND with only 1 cluster)

## Slide 16
CLUSTER ANALYSIS
10 nm
From the binary mask of 0and 1 pixels, the fuction Regionprops
automatically identifies regions separated from other, that we call “Islands”.
For ISLANDs identification:

## Slide 17
CLUSTER ANALYSIS
10 nm : 5 = 2 nm
The code than analyses Island by Island.
2 nm
10 nm
It picks one Island and resizes it of a factor (i.e. 5X).

## Slide 18
CLUSTER ANALYSIS
2 nm
10 nm
The code looks for the localizations that stand inside the mask of the Island.

## Slide 19
CLUSTER ANALYSIS
To each localization:
The code associates a Gaussian curve

## Slide 20
CLUSTER ANALYSIS
loc precision (9nm)
new analysis px (2nm)
σ =
The shape of the Gaussian assigned is defined by the σ, according to the following formula:

## Slide 21
CLUSTER ANALYSIS
x, y localization coordinates
3σ
The Gaussian is centered in the localization x,y coordinates, and extends in a squared ROI of dimension:
roi size = numSigma*σ
By default in the code the roi size is 3σ
.5
.35
.35
.35
.35
.35
.35
.35
.35
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1

## Slide 22
CLUSTER ANALYSIS
New matrix of the summation of Gaussian values belonging to localizations
The code associates the Gaussian curve values to every localization.
.5
.35
.45
.35
.35
.35
.35
.35
.35
.1
.1
.2
.45
.2
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.5
.35
.35
.35
.35
.35
.35
.35
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
The values of different Gaussians are summed together when overlapping
This generates a density map

## Slide 23
CLUSTER ANALYSIS
In each Island,
from the density matrix
the Matlab function regionprops identifies what we call “Clusters”
.5
.35
.45
.35
.35
.35
.35
.35
.35
.1
.1
.2
.45
.2
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.5
.35
.35
.35
.35
.35
.35
.35
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
.1
Then, the function lik_sig retrieves the list of filtered localizations.
If the Number of localizations belonging to each Cluster is
≥ minimum_molecules_per_cluster
the cluster is confirmed.
In each Cluster, the code counts the Number of Localizations.
Clusters with Number of localizations < minimum_molecules_per_cluster are discarded.

## Slide 24
-the Nearest Neighbour Distance (NND) in nm between pairs of closest Clusters, as the mean of cluster’s localizations coordinates
CLUSTER ANALYSIS
Of the filtered Clusters kept in the analysis, the code calculates:
-the coordinates of the Centroid of each Cluster, as the mean of cluster’s localizations coordinates
-the area (nm^2) of each Cluster, as the mean of cluster’s localizations coordinates
To convert px to nm, simply *160 (original pixel size)

## Slide 25
CLUSTER ANALYSIS
The FindCluster.m calculates the NND of InIsland clusters only. For Single clusters, NND is defined as ‘Infinite’ since for definition they have no close neighbours.
N.B.
The calculation of NNDs is done separately for InIslands clusters and for “Single” clusters (=Islands with only 1 cluster inside).
To measure the NND of also Single clusters, the code calls the function DistanceDualColor.m. (explained in the next slide).
The results of NND are put together in the .xyn output files (13rd column of the table).